## Slide 1: SAP HANA Cluster Health Check Introduction & Training
Notes: Change speaker if applicable

## Slide 2: Agenda What Is It? / Architecture Overview Installation, Prerequisites & First Run Core Use Cases (8 scenarios) Understanding Results & Severities Health Check Reference (22 checks) Practical Examples & Troubleshooting Useful Options & Next Steps
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Notes: Marina

## Slide 3
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
SAP HANA Cluster Health Check
What Is It?
Comprehensive, automated health check tool for SAP HANA Pacemaker clusters on RHEL 8/9/10
Key Features:
  22 automated checks covering cluster config, Pacemaker/Corosync, and SAP-specific validations
  Works with live clusters (via SSH), local execution, or offline analysis (via SOSreports)
  Auto-discovers all cluster nodes from a single seed node
  Auto-generated PDF reports with standard or verbose detail
  Multithreaded execution for parallel node checks
  Version detection for RHEL and Pacemaker
  HANA status detection: SID, instance, sidadm user, running processes

## Slide 4
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
SAP HANA Cluster Health Check
Architecture Overview - 5-Step Pipeline
Step 1 - Access Discovery: Discovers local, SSH, Ansible, or SOSreport access to cluster nodes
Step 2 - Cluster Configuration: Node status, quorum, clone config, package consistency (9 checks)
Step 3 - Pacemaker/Corosync: STONITH, resources, fencing, master/slave roles (6 checks)
Step 4 - SAP-Specific: HANA SR status, replication mode, HA/DR hooks, systemd (7 checks)
Step 5 - Report Generation: Summary YAML and PDF reports

## Slide 5
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Getting Started
Installation
Option 1: Using git (recommended)
  git clone https://github.com/mmoster/sap-ha-check.git
  cd sap-ha-check
  ./cluster_health_check.py --local
Option 2: Download without git
  curl -L https://github.com/mmoster/sap-ha-check/archive/refs/heads/main.tar.gz | tar xz
  cd sap-ha-check-main
Prerequisites:
  Python 3.6+ (included in RHEL 8/9/10)
  PyYAML: pip install pyyaml (or dnf install python3-pyyaml)
  fpdf2 (optional, for PDF reports): pip install fpdf2
  SSH key-based access for remote checks

## Slide 6
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Getting Started
First Run
Run locally on a cluster node: ./cluster_health_check.py --local
What happens on first run:
  1. Discovers cluster nodes from Pacemaker configuration
  2. Checks connectivity to all discovered nodes
  3. Collects configuration data from all nodes
  4. Runs all 22 health checks in parallel
  5. Generates summary + PDF report
  6. Caches topology config for faster subsequent runs
Example output:
  PASSED: 22 FAILED: 0 SKIPPED: 0 ERROR: 0
  CLUSTER IS HEALTHY
  PDF report saved: health_check_report_mycluster_1507.pdf

## Slide 7
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Core Use Cases
Use Case 1: Routine Health Check
Run on a live cluster node for a quick validation
Command: ./cluster_health_check.py --local
When to use:
  Daily or weekly operational health checks
  After routine maintenance windows
  Quick sanity check before making changes
What you get:
  Pass/fail summary for all 22 checks
  CRITICAL / WARNING / INFO severity breakdown
  Health status banner (CLUSTER IS HEALTHY / HAS ISSUES)
  Auto-saved PDF report
Tip: First run caches cluster topology. Subsequent runs are faster.

## Slide 8
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Core Use Cases
Use Case 2: Remote Cluster Check
Check clusters remotely via SSH - auto-discovers all members
Option A - Specify nodes directly:
  ./cluster_health_check.py hana01 hana02
Option B - Use a hosts file:
  ./cluster_health_check.py -H hosts.txt
Key behaviors:
  Auto-discovers all cluster nodes from any seed node
  Only one node needed - others found via Pacemaker config
  Uses SSH key-based authentication
  Parallel connectivity checks for speed
  Multi-cluster: prompts for selection if multiple clusters found

## Slide 9
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Core Use Cases
Use Case 3: Offline SOSreport Analysis
Analyze SOSreports without SSH access - ideal for support & post-mortem
Command: ./cluster_health_check.py -s /path/to/sosreports/
When to use:
  Support case analysis
  Post-mortem investigations
  No SSH access available to the cluster
  Historical analysis of saved reports
Supported formats:
  .tar.xz archives (standard SOSreport format)
  .tar.gz and .tar archives
  Pre-extracted SOSreport directories
Tool auto-extracts archives and maps data to the same checks as live analysis.

## Slide 10
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Core Use Cases
Use Case 4: SOSreport Collection Workflow
End-to-end: discover cluster, configure extensions, create & fetch SOSreports
Full workflow: ./cluster_health_check.py -R hana01
Auto-configure: ./cluster_health_check.py -R hana01 --configure-extensions
Workflow steps:
  1. Discovers cluster name and all nodes from the seed node
  2. Checks SSH access to all nodes (skips unreachable ones)
  3. Checks and optionally configures SAP SOSreport extensions
  4. Creates SOSreports in parallel with cluster name as label
  5. Fetches SOSreports via SCP to local ./sosreports/ directory
SAP Extensions add: SAPHanaSR-showAttr output, cluster state snapshots, resource configs

## Slide 11
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Core Use Cases
Use Case 5: Pre-Maintenance Validation
Run before and after maintenance windows to verify cluster state
Before Maintenance:
  ./cluster_health_check.py --local -v
  Establishes baseline state with verbose PDF
  Save as pre-maintenance reference
  Identify any pre-existing issues
After Maintenance:
  ./cluster_health_check.py --local -v
  Verify cluster recovered correctly
  Compare with pre-maintenance report
  Detect any regressions introduced
  Document maintenance outcome

## Slide 12
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Core Use Cases
Use Case 6: Audit & Compliance
Generate detailed PDF reports for compliance documentation
Command: ./cluster_health_check.py --local -v
Verbose PDF includes:
  All 22 checks with full details (not just failures)
  Complete cluster topology and configuration
  Node status and IP addresses
  System replication details
  STONITH/fencing configuration
  Package versions across all nodes
Use for: internal audits, external auditor documentation, management reporting, change management evidence

## Slide 13
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Core Use Cases
Use Case 7: Multi-Cluster Management
Show all discovered clusters: ./cluster_health_check.py -S
Filter by node: ./cluster_health_check.py -S hana01
Key features:
  View all discovered cluster configurations
  Filter by cluster name or node hostname
  Prompts for selection when multiple clusters are found
  Use -D to reset and re-discover all clusters
Use Case 8: Interactive / Exploratory Mode
Command: ./cluster_health_check.py -u
  Scans current directory for SOSreport archives, hosts files, previous results
  Presents an interactive menu to choose what to analyze
  Great for guided setup when unsure where SOSreports are stored

## Slide 14
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Understanding Results
Reading the Output
Healthy cluster output:
  PASSED: 22 FAILED: 0 SKIPPED: 0 ERROR: 0
  CLUSTER IS HEALTHY
Issues detected:
  PASSED: 20 FAILED: 2 SKIPPED: 0 ERROR: 0
  FAILED: CHK_STONITH_CONFIG - STONITH is disabled
Result statuses:
  PASSED - Check completed successfully
  FAILED - Issue detected, action needed
  SKIPPED - Not applicable to this configuration
  ERROR - Check could not complete (missing data or access issue)

## Slide 15
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Understanding Results
Check Severities
CRITICAL - Immediate action required
  Issues that affect cluster availability or data integrity
  Examples: STONITH disabled, node offline, quorum lost, SR status incorrect
WARNING - Should be addressed
  Best practice violations or potential issues
  Examples: Package mismatch, cluster not fully started, resource failures
INFO - Informational
  Context about cluster topology and configuration
  Examples: Cluster type detection (Scale-Up/Scale-Out), HANA installation status

## Slide 16
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Health Check Reference
Cluster Configuration Checks (9)
CHK_CLUSTER_READY [WARNING] - Check if cluster is fully started (not in transition)
CHK_CLUSTER_TYPE [INFO] - Detect Scale-Up vs Scale-Out configuration
CHK_NODE_STATUS [CRITICAL] - Verify all cluster nodes are online
CHK_CLUSTER_QUORUM [CRITICAL] - Verify cluster has quorum
CHK_QUORUM_CONFIG [CRITICAL] - Validate quorum configuration (Scale-Up only)
CHK_CLONE_CONFIG [CRITICAL] - Validate clone resource configuration
CHK_SETUP_VALIDATION [CRITICAL] - Validate against SAP HANA HA best practices
CHK_CIB_TIME_SYNC [WARNING] - Verify CIB updates are synchronized
CHK_PACKAGE_CONSISTENCY [WARNING] - Verify package versions match across nodes

## Slide 17
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Health Check Reference
Pacemaker/Corosync (6) & SAP-Specific (7) Checks
Pacemaker/Corosync Checks:
  CHK_STONITH_CONFIG [CRITICAL] - Verify STONITH/fencing is enabled
  CHK_RESOURCE_STATUS [CRITICAL] - Verify SAP HANA resources are running
  CHK_RESOURCE_FAILURES [WARNING] - Detect failed resource operations
  CHK_ALERT_FENCING [WARNING] - Validate SAPHanaSR-alert-fencing
  CHK_MASTER_SLAVE_ROLES [CRITICAL] - Verify master/slave role consistency
  CHK_MAJORITY_MAKER [CRITICAL] - Validate majority maker constraints (Scale-Out)
SAP-Specific Checks:
  CHK_HANA_INSTALLED [INFO] - Detect HANA installation, SID, instance, sidadm
  CHK_HANA_SR_STATUS [CRITICAL] - Verify HANA System Replication status
  CHK_REPLICATION_MODE [WARNING] - Verify replication mode is sync or syncmem
  CHK_HADR_HOOKS [CRITICAL] - Validate HA/DR provider hooks
  CHK_HANA_AUTOSTART [WARNING] - Validate HANA autostart is disabled
  CHK_SYSTEMD_SAP [WARNING] - Validate SAP Host Agent and systemd config
  CHK_SITE_ROLES [CRITICAL] - Verify site roles consistency

## Slide 18
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Understanding Results
PDF Reports
Standard Report: ./cluster_health_check.py --local
  Shows failed checks with details
  Summary pass/fail counts
  Compact and focused on issues
Verbose Report: ./cluster_health_check.py --local -v
  Shows ALL checks with full details (not just failures)
  Includes complete cluster configuration
  Ideal for audits, compliance, and documentation
What's included in every PDF:
  Cluster name and timestamp
  Node list with status
  Check results table with pass/fail
  Health status banner
  RHEL and Pacemaker version information

## Slide 19
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Practical Examples
Example: Healthy Cluster Output
Command: ./cluster_health_check.py --local
Output:
  Discovering cluster from local node...
  Found cluster: production_hana (hana01, hana02)
  RHEL 9.4 | Pacemaker 2.1.7 | ANGI (sap-hana-ha)
  Step 2: Cluster Configuration Check [9/9 passed]
  Step 3: Pacemaker/Corosync Check [6/6 passed]
  Step 4: SAP-Specific Checks [7/7 passed]
Result:
  PASSED: 22 FAILED: 0 SKIPPED: 0 ERROR: 0
  CLUSTER IS HEALTHY
  PDF report saved: health_check_report_production_hana_1507.pdf

## Slide 20
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Practical Examples
Example: Failed Check (STONITH Disabled)
Output when issues are detected:
  PASSED: 20 FAILED: 2 SKIPPED: 0 ERROR: 0
  FAILED: CHK_STONITH_CONFIG [CRITICAL] - STONITH is disabled
  FAILED: CHK_RESOURCE_FAILURES [WARNING] - 2 failed resource actions on hana01
  CLUSTER HAS ISSUES - REVIEW FAILED CHECKS
Fix STONITH:
  1. Enable STONITH in cluster properties
  2. Configure fencing device
  3. Test with: pcs stonith fence <node>
Fix Resource Failures:
  1. Check pcs status for details
  2. Review /var/log/pacemaker.log
  3. Clear failures: pcs resource cleanup
Re-run health check to verify fixes.

## Slide 21
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Practical Examples
Example: Scale-Out Cluster & Cluster Not Running
Scale-Out Clusters:
  4+ HANA nodes + 1 majority maker node
  Uses SAPHanaController resource agent (vs SAPHana for Scale-Up)
  CHK_MAJORITY_MAKER runs only on Scale-Out topology
  CHK_QUORUM_CONFIG runs only on Scale-Up topology
  Topology detected automatically via resource agent
Cluster Not Running:
  Tool detects Pacemaker/Corosync is not running
  Falls back to corosync.conf for node discovery
  Checks requiring a running cluster are SKIPPED (not FAILED)
  Still runs all checks that work with static configuration
  Useful during planned downtime or startup troubleshooting

## Slide 22
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Tips & Advanced
Useful Options Quick Reference
--local : Run on current cluster node
-s DIR : Analyze SOSreports in directory
-H FILE : Read hosts from file
-u : Interactive mode - scan for resources
-v : Verbose PDF (all checks, full detail)
-d : Debug mode (verbose console output)
-L : List all available health checks
-S [NAME] : Show discovered cluster config
-D : Delete cached config, start fresh
-f : Force rediscovery (ignore cache)
-R NODE : Full SOSreport collection workflow
-F [CLUSTER] : Fetch existing SOSreports from nodes
--no-pdf : Skip PDF report generation

## Slide 23
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Tips & Advanced
Troubleshooting
SSH connection fails:
  Verify key-based SSH access: ssh -o BatchMode=yes <node> hostname
PyYAML not found:
  Install: pip install pyyaml or dnf install python3-pyyaml
No PDF generated:
  Install fpdf2: pip install fpdf2 (optional dependency)
Cluster not detected:
  Pacemaker may not be running. Tool falls back to corosync.conf automatically
Stale cached config:
  Use -D to delete cache and -f to force rediscovery
Wrong cluster selected:
  Use --cluster NAME or -D to reset, then re-run
Tip: Use -d (debug mode) for verbose console output to diagnose issues.

## Slide 24
SAP ALLIANCE TECHNOLOGY TEAM- Markus Moster
Next Steps & Resources
Full Documentation:
  README.md - Complete reference guide
  github.com/mmoster/sap-ha-check
Extend the Tool:
  EXTENDING_HEALTH_CHECKS.md - Create custom health check rules
  check_dispatch.yaml - Topology-aware check dispatch manifest
Quick Start Guide:
  BLOG_HOWTO.md - Step-by-step examples and walkthroughs
Get started now:
  git clone https://github.com/mmoster/sap-ha-check.git
  cd sap-ha-check && ./cluster_health_check.py --local

## Slide 25: Questions?

## Slide 26: Thank you